Indirect Visual Odometry with Optical Flow
Indirect Visual Odometry with Optical Flow
Chenguang Huang, Andong Tan
München, 22. July 2019

---
Overview
Overview
1. Introduction
1.1 Lukas Kanade Method for Optical Flow
1.2 Project Pipeline
1.3 Parameter and strategy
2. Result
2.1 Precision Comparison
2.2 Execution Time Comparison
2.3 Visualization Comparison
3. Conclusion

---
1 Introduction
1.1 Lukas Kanade method for optical flow
Input: two images, key points in one image
Output: the key points in the other image(the motion of the key points).
Output key point position in the other image
Input key point position in one image

---
1.1 Lukas Kanade method for optical flow
Inspiration in SLAM:
replace feature descriptors matching with optical flow method!
Output key point position in the other image
Input key point position in one image

---
1 Introduction_clipboard1
Keypoints detection in every key frame:
no
yes
Keyframe?
……
First image?
no
yes
1 Calculate key points in left image
according to left image in last time step (OF)
2 Separate the left image into cells and detect
new points in empty cells
3 Calculate the keypoints in right image (OF)
according to left image
4 Compute essential matrix and find inlier
5 Localize camera
6 Create new landmarks
7 Optimization
(8 frame-frame triangulation)
1 Key points detection in left image
2 Calculate key points in right image according
to left image (OF)
3 Compute essential matrix, find inlier
4 Localize camera
5 Initialize landmarks

---
Use optical flow and keypoints detection in key frame:
Keyframe?
yes
no
1 Calculate key points in left image
according to left image in last time step (OF)
2 Separate the left image into cells and
calculate the number of empty cells
3 (no calculation of essential matrix)
Because no relative pose between frame
4 Localize camera
6 If not enough key points or inliers or
too many empty cells && optimization is not
running and not finished, set the next frame
as key frame
First image?
……

---
1.2 Project pipeline: first key frame
Step 1: detect key points in left image
Left image
Right image
Time 0

---
1.2 Project pipeline: first key frame
Step 2: use optical flow to get corresponding key points in right image
Left image
Right image
.
.
.
Time 0

---
1.2 Project pipeline: first key frame
Step 3: check epipolar constraint and find inlier
Left image
Right image
Time 0

---
1.2 Project pipeline: first key frame
Step 4: localize camera(initialize the first left camera pose with identity matrix)
Left image
Right image
Time 0

---
1.2 Project pipeline: first key frame
Step 5: triangulate landmarks
…...
Left image
Right image
Time 0

---
1.2 Project pipeline: second and later key frame
Step 1: optical flow to next left frame
Left image
Right image
Time t-1
Time t

---
1.2 Project pipeline: second and later key frame
Step 1: optical flow: backward check
Left image
Right image
Time t-1
abandon
Time t

---
1.2 Project pipeline: second and later key frame
Step 2: make grid & detect key points in empty cells
Left image
Right image
Time t-1
Empty cells
Time t
Detect new
key points

---
1.2 Project pipeline: second and later key frame
Step 3: use optical flow to find the corresponding key points in the right image
Left image
Right image
Time t-1
Newly detected
Compute from last frame
Time t

---
1.2 Project pipeline: second and later key frame
Step 4: use epipolar constraint to find inliers
Left image
Right image
Time t-1
Inliers
Time t

---
1.2 Project pipeline: second and later key frame
Step 5: localize camera
Left image
Right image
Time t-1
Use the key
points that
already has
landmarks
to localize
camera
Time t

---
1.2 Project pipeline: second and later key frame
Step 6: add observation and create landmarks
Left image
Right image
Time t-1
Add observation
Create new
landmarks
Time t

---
1.2 Project pipeline: non key frame
Step 1: use optical flow to get corresponding key points last time step of left frame
Left image
Right image
Time t-1
Time t

---
1.2 Project pipeline: second and later key frame
Step 2: make grid in left image and count the number of empty cells
Left image
Right image
Time t-1
# of empty cells
Time t
Don’t detect new
key points

---
1.2 Project pipeline: second and later key frame
Step 2: make grid in left image and count the number of empty cells
Left image
Right image
Key framing strategy
Time t-1
# of empty cells
If greater than
threshold, make
 next frame
key frame
Time t

---
1.2 Project pipeline: second and later key frame
Step 5: localize camera
Left image
Right image
Time t-1
localize
camera
Time t

---
1.3 Parameter and strategy
1.3.1 Grid shape: retangle vs square
pixel x pixel
30 x 47
32 x 32
0.14
rmse
0.11

---
1.3 Parameter and strategy
1.3.2 Key points detection: in whole image vs in each cell
Detect in whole image
Detect in empty cells respectively
Then only keep key points in empty cells
0.1139
rmse
0.1116

---
1.3 Parameter and strategy
1.3.3 Key framing: use grid vs use only inliers number
# of localization inliers
# of empty cells
If greater than
threshold, make
 next frame
key frame
If smaller than
threshold, make
 next frame
key frame
0.11
rmse
0.43

---
2 Result
2.1 Precision comparison
Basic parameters
image height / (pixel)	image width / (pixel)	grid size / (pixel x pixel)	Minimum number of key points
480	752	32 x 32	100
Strategy
1. Square grid
2. Add key points in each cell
3. Use empty cells number to decide next key frame

---
2 Result
2.1 Precision comparison
Variation parameters: maximum empty cells percentage*
Max empty cells (%)	0.35	0.4	0.42	0.44	0.46	Exercise 5
rmse	0.1303	0.1295	0.1099	0.1563	0.1304	0.1012
*maximum empty cells percentage: when the empty cells percentage exceeds this
 value and optimization is finished, make next frame key frame

---
2 Result
2.1 Precision comparison

---
2 Result
2.2 Execution time comparison
2.2.1 Detection time
Max empty cells (%)	0.35	0.4	0.42	0.44	0.46	Exercise 5
detection time / (seconds)	3.03643	2.73232	2.43286	2.62328	2.26326	44.0214

---
2 Result
2.2 Execution time comparison
2.2.2 Optimization time
Variation parameters: maximum empty cells percentage*
Max empty cells (%)	0.42	Exercise 5
Opt. time(s)	305.043	65.8619
# landmarks	290657	221886
# observation	1939460	559563
# keyframe	414	170

---
2 Result
2.2 Execution time comparison
2.2.3 Frame to frame (f2f) optical flow time
Ex. 5 / Feature Matching time(s)	5.79
f2f optical flow time(s)	117.4~143.1

---
2 Result
2.3 Visualization comparison
Maximum empty cells percentage: 0.42

---
2 Result
2.3 Visualization comparison
Exercise 5

---
2 Result
2.3 Visualization comparison
Exercise 5
Maximum empty cells number: 0.42

---
2 Result
2.3 Visualization comparison

---
2 Result
2.3 Visualization comparison
Exercise 5
Maximum empty cells number: 0.42

---
3 Conclusion
What we did in this project:
1. We use Lucas and Kanade Optical Flow method to replace normal feature matching in slam.
2. We try different key framing strategies: use grid or only inliers.
3. We try different setups for the pipeline, such as shape of grid, key points detection strategies.
4. We visualize the ground truth and estimated trajectories of camera and do analysis.

---
3 Conclusion
What we can do in the future:
1. implement optical flow manually, using intensity invariant optical flow to make the pipeline more stable.
2. try to implement frame to frame triangulation: using left images at different time step to triangulate new landmarks.

---
Q&A
Any question?

---
Thank you for your attention!