Indirect Visual Odometry with Optical Flow
Indirect Visual Odometry with Optical Flow
Chenguang Huang, Andong Tan
München, 26. July 2019
弄个全局变量
全部打印出来
直接运行，
截图
数据进表格

---
Overview
Overview
1. Introduction
1.1 Lukas Kanade Method for Optical Flow
1.2 Project Pipeline
2. Result
2.1 Precision Comparison
2.2 Execution Time Comparison
2.3 Visualization Comparison
3. Conclusion

---
1 Introduction
1.1 Lukas Kanade method for optical flow
Input: two images, key points in one image
Output: the key points in the other image(the motion of the key points).
Output key point position in the other image
Input key point position in one image

---
1.1 Lukas Kanade method for optical flow
Inspiration in SLAM:
replace feature descriptors matching with optical flow method!
Output key point position in the other image
Input key point position in one image

---
1 Introduction_clipboard0
1.1 Lukas Kanade method for optical flow
Basic mathematical principle
A method to estimate the motion of object in image. It is based on one assumption:
the brightness of a moving point remains constant over time
Derivative with respect to time

---
1.1 Lukas Kanade method for optical flow
Solve this function for v

---
1 Introduction_clipboard1
Keypoints detection in every key frame:
Keyframe?
yes
no
……
First image?
yes
no
1 Calculate key points in left image
according to left image in last time step (OF)
2 Separate the left image into cells and detect
new points in empty cells
3 Calculate the keypoints in right image (OF)
according to left image
4 Compute essential matrix and find inlier
5 Localize camera
6 Create new landmarks
7 Optimization
(8 frame-frame triangulation)
1 Key points detection in left image
2 Calculate key points in right image according
to left image (OF)
3 Compute essential matrix, find inlier
4 Localize camera
5 Initialize landmarks

---
Use optical flow and keypoints detection in key frame:
Keyframe?
yes
no
1 Calculate key points in left image
according to left image in last time step (OF)
2 Separate the left image into cells and
calculate the number of empty cells
3 (no calculation of essential matrix)
Because no relative pose between frame
4 Localize camera
6 If not enough key points or inliers or
too many empty cells && optimization is not
running and not finished, set the next frame
as key frame
First image?
……

---
1.2 Project pipeline: first key frame
Step 1: detect key points in left image
Left image
Right image
Time 0

---
1.2 Project pipeline: first key frame
Step 2: use optical flow to get corresponding key points in right image
Left image
Right image
.
.
.
Time 0

---
1.2 Project pipeline: first key frame
Step 3: check epipolar constraint and find inlier
Left image
Right image
Time 0

---
1.2 Project pipeline: first key frame
Step 4: localize camera(initialize the first left camera pose with identity matrix)
Left image
Right image
Time 0

---
1.2 Project pipeline: first key frame
Step 5: triangulate landmarks
…...
Left image
Right image
Time 0

---
1.2 Project pipeline: second and later key frame
Step 1: use optical flow to get corresponding key points last time step of left frame
Left image
Right image
Time t-1
Time t

---
1.2 Project pipeline: second and later key frame
Step 1: use optical flow to get corresponding key points last time step of left frame(backward check)
Left image
Right image
Time t-1
abandon
Time t

---
1.2 Project pipeline: second and later key frame
Step 2: make grid in left image and detect key points in empty cells
Left image
Right image
Time t-1
Empty cells
Time t
Detect new
key points

---
1.2 Project pipeline: second and later key frame
Step 3: use optical flow to find the corresponding key points in the right image
Left image
Right image
Time t-1
Time t

---
1.2 Project pipeline: second and later key frame
Step 4: use epipolar constraint to find inliers
Left image
Right image
Time t-1
Inliers
Time t

---
1.2 Project pipeline: second and later key frame
Step 5: localize camera
Left image
Right image
Time t-1
Use the key
points that
already has
landmarks
to localize
camera
Time t

---
1.2 Project pipeline: second and later key frame
Step 6: add observation and create landmarks
Left image
Right image
Time t-1
Add observation
Create new
landmarks
Time t

---
1.2 Project pipeline: non key frame
Step 1: use optical flow to get corresponding key points last time step of left frame
Left image
Right image
Time t-1
Time t

---
1.2 Project pipeline: second and later key frame
Step 2: make grid in left image and count the number of empty cells
Left image
Right image
Time t-1
# of empty cells
Time t
Don’t detect new
key points

---
1.2 Project pipeline: second and later key frame
Step 2: make grid in left image and count the number of empty cells
Left image
Right image
Time t-1
# of empty cells
If greater than
threshold, make
 next frame
key frame
Time t

---
1.2 Project pipeline: second and later key frame
Step 3: use optical flow to find the corresponding key points in the right image
Left image
Right image
Time t-1
Time t

---
1.2 Project pipeline: second and later key frame
Step 4: use epipolar constraint to find inliers
Left image
Right image
Time t-1
Inliers
Time t

---
1.2 Project pipeline: second and later key frame
Step 5: localize camera
Left image
Right image
Time t-1
localize
camera
Time t

---
2 Result
2.1 Precision comparison
Basic parameters
image height / (pixel)	image width / (pixel)	grid size	Minimum number of key points
480	752	16x16	100

---
2 Result
2.1 Precision comparison
Variation parameters: maximum empty cells number*
Maximum empty cells number	50	100	150	250	Exercise 5
rmse	0.1266	0.1261	0.1218	0.1223	0.1012
*maximum empty cells number: when the empty cells number exceeds this
 value and optimization is finished, make next frame key frame

---
A picture about optical flow
Some lines
Stereo
Frame to frame

---
A picture about cell
Empty cells ----- detection
not enough key points/inliers/
too many empty cells && optimization is not
running and not finished,

---
2 Comparison
2 Comparison
2.1 Precision Comparison
2.2 Execution Time Comparison
2.3 Visualization Comparison

---
Parameter Sets (Optical flow version)
Parameter Sets (Optical flow version)
	Set 1	Set 2	Set 3	Set 4	Set5
Cell width:	47
Cell height:	30
Num of cells:	16*16	16*16
Min number of key points:	200	200
Max number of empty cells:	100	90	100	105	110
Precision level in key point detection:	0.001

---
Parameter Sets (Direct detection version)
Parameter Sets (Direct detection version)
	Set D-1	Set D-2	Set D-3	Set D-4
Default…
Precision level in key point detection:	0.001

---
2.1 Precision Comparison_clipboard0
2.1 Precision Comparison
Optical Flow Version:
	Set 1(100)	Set(90)	Set3(100)	Set4(105)	Set5(110)
Rmse: just this	5.26	6.84	5.828	5.925	5.602
Mean:	0.105	0.135	0.116	0.119	0.114
Min:	0.01	0.010	0.022	0.028	0.016
Max:	0.24	0.290	0.253	0.271	0.242
Precision level in key point detection:	0.001

---
2.1 Precision Comparison_clipboard0
2.1 Precision Comparison
Optical Flow Version:
	Set 1(100)	Set(90)	Set3(100)	Set4(105)	Set5(110)
Rmse: just this	5.26	6.84	5.828	5.925	5.602
Mean:	0.105	0.135	0.116	0.119	0.114
Min:	0.01	0.010	0.022	0.028	0.016
Max:	0.24	0.290	0.253	0.271	0.242
Precision level in key point detection:	0.001

---
2.1 Precision Comparison
2.1 Precision Comparison
Direct Detection Version:
Parameter set: Set 1 Set 2 Set 3 Set 4
Rmse: 5.53(5.26) 5.95
Mean: 0.107(0.105) 0.118
Min: 0.018(0.01) 0.020
Max: 0.288(0.24) 0.359
CHECK Rmse 0.1
*Rmse: root mean square error

---
2.2 Execution Time Comparison
2.2 Execution Time Comparison
Optical Flow Version:
Parameter set: Set 1 Set 2 Set 3 Set 4
Execution time(s)
Detection: 5.83
Stereo match: 39.28
Frame to frame match: 204.78
Localization: 24.29
Add landmark: 0.18
Optimization: 271.27
Other
Total num. of opt. landmark: 243428
Total num. of opt. observation: 2049019

---
2.2 Execution Time Comparison
2.2 Execution Time Comparison
Direct Detection Version:
Parameter set: Set 1 Set 2 Set 3 Set 4
Execution time(s)
Landmark projection: 2.93
Detection: 66.6086 (5.83)
Stereo match: 0.178 (39.3)
Landmark match time: 7.54
Localization: 12.35 (24.29)
Add landmark: 0.072 (0.18)
Optimization: 103.907 (271.27)
Other
Total num. of opt. landmark: 222638 (243428)
Total num. of opt. observation: 561968 (2049019)

---
2.3 Visualization Comparison
2.3 Visualization Comparison
        Demo